## Slide 1: Team Aakashwani: CAN-7USAT
Hardware & PCB Layout Planning Session
Transitioning from PDR to Detailed Design

## Slide 2: 1. Our Dual-Pack Power Architecture
Our PDR mandates a strict separation to prevent brown-outs:
Pack A (Avionics): 2S 18650 (3.4 Ah). Powers the ESP32-S3, sensors, and radios.
Pack B (Drone): 2S 18650. Dedicated solely to the 4-in-1 ESC and BLDC motors.
Layout Rule #1: These two power nets MUST remain physically isolated on the PCBs. Motor current spikes cannot be allowed to reach the 5V BEC.

## Slide 3: 2. Avionics Power Chain (Pack A)
How power routes to the brains:
Path: XT30 (J1) -> Fuse -> Ext Switch -> INA260 -> 5V/3A BEC -> AMS1117-3.3
Monitoring: We must place the INA260 and MAX17048 close to the battery input for accurate V/I and SoC telemetry.
Buzzer: Powered directly from VBAT. Needs a dedicated high-current trace, isolated from sensor 3.3V lines.

## Slide 4: 3. The Star-Point Ground
The most critical part of our dual-pack system:
Although Pack A and Pack B are separate, the ESC needs to read PWM signals from the ESP32.
We must implement a Single Star-Point Ground where Avionics GND meets ESC GND.
Layout Rule #2: Do not create multiple ground bridges between the systems, or we will create a ground loop that invites EMI.

## Slide 5: 4. The H-Shaped PCB Assembly
Our mechanical structure uses a rigid H-shaped PCB configuration:
  Right Board (|): Power Distribution. Handles noisy Pack B, ESC, regulators, and high currents.
  Left Board (|): Avionics & CDH. Houses ESP32-S3, XBee, and CC1101, physically isolated from motor noise.
  Middle Board (-): Sensor Bridge. Castellated edges bridge the two side-boards together.
OPTIMIZATION: The middle board sits on the central axis of the CanSat. This is the perfect mathematical center for the BNO085 IMU, preventing centrifugal offset errors during rotation!

## Slide 6: 5. Sensor Bridge PCB Details
Sensors: BMP585, BNO085, SHT4x, SGP41, Pitot DP.
All operate on 3.3V. Total draw < 0.3 W.
I2C Routing: We have two I2C buses. Keep traces short, away from the edges (EMI from carbon rods), and ensure pull-up resistors are correctly placed.
Decoupling: 0.1µF capacitors placed at the VCC pin of EVERY single sensor IC.

## Slide 7: 6. RF Interference Mitigation
Radios: XBee 3 Pro (2.4 GHz) + CC1101 (433 MHz) + Edgehax GNSS.
Layout Rule #4: NO COPPER underneath antennas! The PCB must have keep-out zones on all layers below the XBee and GNSS patch antennas.
SPI routing for CC1101 and microSD must be shielded by ground planes to prevent high-speed clock noise from deafening the GNSS.

## Slide 8: 7. Mechanical Integrity
As per PDR: 'No press-fit or friction-fit anywhere'.
Connectors: All harnesses must use positive-locking connectors (JST-XH/XT30). No spring contacts.
Mounting: M3 screws into brass heat-set inserts (≥ 4 points/board). Keep copper traces away from the mounting holes to prevent shorts if a screw bites into the PCB.

## Slide 9: 9. KiCad: Hierarchical Schematics
Problem: Our current schematic is one massive sheet. This is a nightmare for a 3-board production.
Solution: We must use KiCad's Hierarchical Sheets.
  Create a 'Root' block diagram sheet.
  Sheet 1 (Right Board): Power, ESC, Regulators.
  Sheet 2 (Middle Board): Sensor Bridge, I2C pull-ups.
  Sheet 3 (Left Board): ESP32, XBee, CC1101.
Why? It allows different team members to work on different sheets simultaneously and maps perfectly to our H-shaped boards.

## Slide 10: 10. The KiCad Execution Plan
How we actually build this step-by-step:
Step 1: Custom Footprints. We must design 1:1 courtyard footprints for our modules (like the XBee and ESC) to guarantee they fit inside the 140mm cylinder.
Step 2: Hierarchical Schematic Entry. (Assign pins and verify all decoupling caps).
Step 3: Board Setup (4-Layer Stackup). Set our constraints (trace widths, clearance).
Step 4: Layout & Routing. Place components first, then route.

## Slide 11: 11. Why 4 Layers?
For a high-density, mixed-signal CanSat, 2 layers is too risky.
Layer 1 (Top): Components and short signal traces.
Layer 2 (In1): Solid Ground Plane (GND). Provides a direct, low-impedance return path for every signal. Kills EMI.
Layer 3 (In2): Power Plane (3.3V / 5V). Delivers clean power without needing thick traces everywhere.
Layer 4 (Bottom): Remaining signal traces and connectors.
Cost: JLCPCB/PCBWay 4-layer boards are now incredibly cheap. The reliability gain is mandatory for our mission.

## Slide 12: 12. Electrically Bridging the Boards
How does the Middle board connect to the Left and Right boards in KiCad?
Castellated Holes (Half-Vias): We place standard via pads on the exact edge of the middle board.
When manufactured, the router cuts through the vias, leaving copper half-cylinders exposed on the edge.
Assembly: We slide the middle board between the two side boards and solder the edges together like a surface-mount component.
KiCad Trick: We must align the castellated edge pins on the middle board perfectly with mating surface-mount pads on the side boards.

## Slide 13: 13. Design for Testability (DFT) & Thermals
How we ensure the board survives the +60°C thermal soak and the software team can actually debug it:
Test Points: The software team needs to run HIL (Hardware-in-the-Loop) simulations. We MUST add exposed copper pads (Test Points) for GND, 3.3V, 5V, TX, RX, SDA, and SCL.
  Without test points, debugging requires soldering wires to microscopic pins, which ruins boards.
Thermal Vias: The 5V BEC and the ESC will generate significant heat in a closed CanSat cylinder.
  We must place thermal vias (tiny copper-plated holes) directly underneath these hot components to dump their heat into the massive internal Ground plane (Layer 2), turning the whole PCB into a heatsink.

## Slide 14: 14. Post-Design Power Estimation
How do we verify our power budget before the board is even manufactured?
1. The Living BOM (Spreadsheet): Every time a component is added to KiCad, its 'Max Active Current' and 'Sleep Current' from the datasheet MUST be added to our master spreadsheet.
2. Duty Cycle Math: A radio drawing 200mA during TX, but only transmitting 10% of the time, averages 20mA. We must calculate Average Current for battery life, and Peak Current for regulator sizing.
3. KiCad PDN Calculator: Once traces are drawn, we use KiCad's built-in calculator to ensure a long trace doesn't cause a voltage drop that browns out a sensor.
4. SPICE Simulation: If we design any custom analog filtering, we simulate it (e.g., LTspice/ngspice) before sending gerbers to fabrication.

## Slide 15: 15. Planning Tools & Master Spreadsheet
To execute this, we use standard industry tools:
Saturn PCB Toolkit: Everyone routing a board MUST use this to calculate trace widths.
TI WEBENCH: Use this to simulate the 5V BEC thermal output.
The Master Power Budget Spreadsheet:
--> CLICK HERE TO OPEN THE MASTER SPREADSHEET <--

## Slide 16: 16. KiCad Action Items
Next steps for the hardware team:
[ ] Verify castellated edge footprints for the H-bridge assembly.
[ ] Create 1:1 courtyard footprints in KiCad to guarantee zero-collision.
[ ] Assign person to route the Right Board (Power/Actuator).
[ ] Assign person to route the Left Board (Avionics) and Middle Board (Sensor Bridge).